## Slide 1
Korean Icebreaker – ARAON -
KOPRI
December, 2009

## Slide 2
_
_
_
_

## Slide 3
Korean Icebreaker ARAON
2

## Slide 4
Purpose
- To execute multidisciplinary research survey
in the both polar regions
- Logistics support for the Antarctic station
Period : 2004~2009 (6 yrs)
Budget : 100 mil USD
‘Ara’ (sea) + ‘On’ (all) = All the sea

## Slide 5
Classification : KR PL-10
(1 m depth icebreaking in 3 knot, Dnv Polar 10)
Propulsion : Azimuth Thruster
- Diesel electric plant : 10 MW (5 MW x 2)
DP-2 System
Tonnage : 7,847 GRT
Manning : 85 persons (25+60)
Service Speed : 12 knot
Endurance : 20,000 nm (70 days)
Length: 111 m
Helicopter
Container: 31 TEU
Barge
Work Boat
25ton Crane
Breadth: 19 m
Korean Icebreaker, ‘ARAON’ - 1
Notes: 그림 적절히 수정 및 재배치

## Slide 6
Korean Icebreaker, ‘ARAON’ - 2

## Slide 7
Higher Tensile Steel
- Ice strengthening area and transverse structural members
- Thickness : 39.5 mm in max.
- Material (RE 36, - 40 ℃) : normalized steel or TMCP steel
Hull Stress & Ice Load Monitoring System
- Realtime monitoring and alert while ice breaking
- Keeping ice load data on cruising route
Korean Icebreaker, ‘ARAON’ - 3

## Slide 8
Sensors fitted on Hull Bottom
- Compact and no interferance
- Ice protection of bottom sensors from ice load
Working Deck
- Wooden deck
- Close for winches
- Room for controlling & monitoring
Heeling System
- Air-blow type
- 7 °heeling from port to starboard
during 3 minutes
Korean Icebreaker, ‘ARAON’ - 4

## Slide 9
Seismic Z-Frame
Working Boat (6 prn)
Safety Boat (85 prn)
Cargo Space
Hatch Cover
25t crane
CTD Crane
A-Frame
3t Crane
10t Crane
A-Frame
Oceanography : CTD with water sampler, etc.
Geophysics : Multi-channel seismic system, etc.
Marine Geology : Multi-beam echo sounder, etc.
Biology : MOCNESS, Sea soar, etc.
Monitoring, Analyzing equipment : Weather Station, etc.
Korean Icebreaker, ‘ARAON’ - 5

## Slide 10
Korean Icebreaker, ‘ARAON’ - 6
Equipment | Specification | Equipment | Specification
ADCP/LADCP | Freq:38kHz | Salinometer | Measurement Range: 0.0001:1.15 Conductivity Ratio 0.004 to 76mS/cm 0.005 to 42 Equivalent Practical PSU
Scientific Fish Finder | Freq:38,120,200kHz | Acoustic Synchronizer System | Synchronizing up to 12 acoustic system Better than 1 msec timing resolution
Low Fre. Omni-Directional Fishery Sonar | Freq:24/26/28kHz | Marine Gravity Meter | Resolution:0.01mGal Static Repeatability:0.05mGal Accuracy at Sea:1.00mGal
Multi-Beam Echo Sounder in cluding Sub-Bottom Profiler) | Freq:12kHz Freq:2.5kHz ~ 7kHz | Marine Magnetometer | Absolute accuracy:0.2nT Sensitivity:0.01nT Resolution:0.001nT
Precision Depth Recorder | Freq:12/38kHz | Wavemeter | Significant Wave Height - Range:0~5m, Accuracy:0.25~0.5m - Range:Above 5m, Accuracy:10%
Compressor System | GA90W / Air Receiver / CT | Underwater Undulating Instrument System | Towing speed:0.5 ~ 10knot Operating Depth:0 ~ 400m
Aerosol Sizing Instrument | Heating Control:0~300 ℃ | Multi-Channel Seismic System | Streamer CH:120 Air Gun Vol:1200 cu in
LIDAR | Range:12km (Less than) wavelength:532nm | TV Grab | working depth:~6000m Grab size:2 X 2ft

## Slide 11
Korean Icebreaker, ‘ARAON’ - 7
Equipment | Specification | Equipment | Specification
Attitude and Positioning System | Heading Accuracy:0.02 ℃ Roll/Pitch Accuracy:0.02 ℃ Heave Accuracy:5cm or 5% | MOCNESS | Net size:333 micron mesh No of Net:9 Length of Net:6.0m
LAN system | Master/Slave Server/Ship's Signal Interface Unit/ | Satellite Receiver | Radome attenuation:~0.15dB L-Band Input Freq:1680~1710Mhz S-Band Input Freq:2207~2267Mhz
CTD | Temperature:-5 ~ 35℃ Conductivity:0 ~ 7 S/m Pressure:0 ~ 10500 meter | Sea Water Analyze | Take 120 sample cups up to 5mL Fiber optic detector for Nutrient
Weather station |  | Data cable | 
Sub-bottom profiler |  | pCo2 System | 
ITRAC Core Scanner(Second Generation) |  | Thermo-Salinograph | 
Streamer Winch |  | Umblilical Winch | 
Magnetometer Winch |  | Gun Array | 
Deep Sea Winch |  | Electro-Optic Cable Winch | 
Small Empty Winch |  | Small Coaxial Cable Winch | 
CTD Winch |  | CTD Crane | 
Stern A-Frame |  | CTD Handling System | 
Winch Monitoring System |  | Uncontaminater Seawater System | 

## Slide 12
Jan. 2008 : Steel Cutting
May 2008 : Keel Laying
Jun. 2009 : Launching
Oct. 2009 : Delivery
2007 : Shipbuilding Start
KOPRI/HANJIN/KMS
2004 ~ 2005 : Concept & Basic Design
2003 : Feasibility Study
Jan ~ Feb. 2010 : Ice trial
Korean Icebreaker, ‘ARAON’ - 8
Notes: 연도순이 위아래로 지그재그 배치되어 아주 어지러운데… 한쪽으로 배치 요망!

## Slide 13
Korean Icebreaker, ‘ARAON’ - 9

## Slide 14
Changing roles of Antarctic sea ice in global changes
Amundsen sea (abt. 20 days)
Major Research Field(draft)
Antarctic marine ecosystem survey
Shetland islands (abt. 20 days)
Pacific meridional transect program
Monitoring in the Arctic ocean
Bering sea, Arctic sea (abt. 40 days)
Greenhouse gas control,
Antarctic bathymetry & sea-bottom mapping
Bellingshousen sea (abt. 20 days)
Multidisciplinart survey on pacific-Antarctic ridge
Bransfield strait (abt. 20 days)
Environmental changes of Antarctic penn. Ice shelves
Weddell sea (abt. 20 days)
“in each area international
cooperation is actively sought”

## Slide 15
conduct Ice trial & assist site survey
Main duty
Time plan | Activities
19th, Dec ~ 7th, Jan | Incheon → Christ Church
8th, Jan ~ 11th, Jan | Christ Church
12th, Jan ~ 23rd, Jan | Christ Church → Cape Burks
24th, Jan ~ 2nd, Feb | Ice trial and site survey
3rd, Feb ~ 12th, Feb | Cape Burks → Christ Church
13th, Feb ~ 15th, Feb | Christ Church
16th, Feb ~ 7th, Mar | Christ Church → Incheon
CB (24th, Jan ~ 2nd, Feb)
- Conduct ice trial
& assist site survey
10 days
CHCH(12th, Jan)
5 days
10 days
Joint point : ARAON
and AK
Korean Icebreaker, ‘ARAON’ - 11

## Slide 16
‘The Light of Pole’ means global dynamics, the future of polar research and the hope of polar research
Korean Icebreaker, ‘ARAON’ - 12

## Slide 17
Thank you
Thank you